## Slide 1
Application of targeted DART–TQ MS to food safety and authenticity: Two Case Studies
Anna Luparelli1, William Matteo Schirinzi1, Laura Quintieri1, Alexandre Verdu2, Linda Monaci3*
1Institute of Sciences of Food Production, National Research Council (ISPA-CNR) Bari, Italy;
2Bruker France S.A.S. Applied Mass Spectrometry, Wissembourg Cedex, France;
*3Institute of Biomembranes, Bioenergetics and Molecular Biotechnologies, National Research Council (IBIOM-CNR), Bari, Italy.

## Slide 2
Coupling DART-MS:
A Powerful Tool for Rapid Analysis
✨Why is DART-MS so attractive?
Direct Analysis in Real Time Mass Spectrometry (DART-MS) is a relatively recent technique (introduced in 2005) designed for rapid mass spectral analysis under ambient conditions.
Quantitative capabilities of DART-MS to be further investigated
The ionization amount of a target analyte correlates with the molecular ion peak intensity.
✅ Ionization | Ambient pressure; direct desorption/ionization (no vacuum chamber needed)
✅Speed | Fast MS fingerprint in seconds (Gross, 2014)
✅Simplicity | Only two core components: Ion Source + MS
✅No Chromatography | Chromatography-free → no separation, no long runs
✅Sample Prep | Minimal or none → ideal for rapid screening
✅Throughput | Compatible with multiwell sample cards for high-throughput workflows

## Slide 3
Research Background & Motivation
Tipically combined with HR MS platforms: Q TOF, TOF, Orbitrap based Mass spectrometers for qualitative and confirmatory analysis in the field of food safety and food quality.
Rare reports about quantitative analysis in food by DART-MS technology.
The launch on the market of the DART TQ MS (EVOQ) has prompted in investigating instrumental capabability of such configuration in quantitative analysis of contaminants/adulternats in foods.

## Slide 4
Case Studies
Food authenticity:
detection of adulterated saffron by low-cost spices
Food safety:
determination of biogenic amines in tuna fish, with a focus on histamine.
2
1

## Slide 5
Case Study 1
Food authenticity:
detection of adulterated saffron by low-cost spices
1
The aim of this study was to develop a fast, robust, and chromatography-free DART–MS/MS method for the targeted detection of turmeric and safflower adulteration in saffron.

## Slide 6
DART-MS/MS analysis
Add 5mL of EtOH/H₂O 70/30 (v/v) to 50 mg of spice powder
    Shaking 15 min
    Centrifuge 5min at 13000rpm
    Filter on PTFE 0,45uM
Serial dilution of saffron extract intentionally adulterated with increasing concentrations of safflower and turmeric extracts.
Extract deposition
Safflower 100%
Saffron 100%
Turmeric 100%
Quick extraction
Materials and Methods
Food authenticity:
detection of adulterated saffron by low-cost spices
1
Case Study 1

## Slide 7
Materials and Methods
Identification of potential markers tracing for safflower and turmeric in saffron
Food authenticity:
detection of adulterated saffron by low-cost spices
1
Calibration curves in saffron adulterated with safflower or turmeric powder
Application of the developed multi-target method to adulterated saffron samples
STEP 1
STEP 2
Identification of ion transitions for each adulterating compound
STEP 5
STEP 3
Optimization of DART and MS settings for MRM-DART TQ MS/MS analysis
STEP 4
safflower
turmeric
DART-TQ parameters

## Slide 8
Food authenticity:
detection of adulterated saffron by low-cost spices
1
Selection of Safflower and Turmeric Markers
Full scan MS spectra obtained in the mass range 100–600 m/z in pure saffron (A), safflower (B) and turmeric (C).
Results
Candidate markers for turmeric to be further investigated:
Candidate markers for safflower to be further investigated:
    116,2 m/z
    198,2 m/z
    296,2 m/z
    446,4 m/z
    235,3 m/z
    309,0 m/z
    338,9 m/z
    369,0 m/z

## Slide 9
Candidate markers for turmeric to be further investigated:
Candidate markers for safflower to be further investigated:
Food authenticity:
detection of adulterated saffron by low-cost spices
1
50% and 20%
safflower fortification, 10 replicates of analysis
CV% intraday
CV% interday= 15% with IS correction.
Results
Fortified saffron extracts and calibration curves
Linearity
Quantifier ion transition (safflower): 116.2/70.1 (m/z)
50% safflower fortification,
5 replicates of analysis in 3 consecutive days
Precision
 | NO IS | IS
50% | 17% | 11%
20% | 6% | 8%
Caffeine ion transition: 195/138 (m/z)

## Slide 10
Candidate markers for turmeric to be further investigated:
Candidate markers for safflower to be further investigated:
Food authenticity:
detection of adulterated saffron by low-cost spices
1
Results
Production of Matrix-Matched Calibration Curves in Saffron Powder
Ion transition | Calibration curve equation | R² | LOD % (w/w) | LOQ % (w/w)
Safflower in saffron | Safflower in saffron |  | Safflower in saffron | Safflower in saffron
116/70 | y = 0,0717 (±0,0063) x - 0,1786 (±0,174) | 0,985 | 7 | 24
446/116 | y = 0,1014 (±0,0067) x - 0,2633 (± 0,185) | 0,991 | 5 | 18
Turmeric in saffron | Turmeric in saffron |  | Turmeric in saffron | Turmeric in saffron
339/178 | y = 1,4027 (± 0,052) x - 3,5298 (± 1,445) | 0,997 | 3 | 10
368/285 | y = 4,2545 (± 0,253) x- 5,9038 (± 0,965) | 0,993 | 5 | 16

## Slide 11
Candidate markers for turmeric to be further investigated:
Candidate markers for safflower to be further investigated:
    116,2
    198,2
    296,2
    446,4
Food authenticity:
detection of adulterated saffron by low-cost spices
1
Results
Recovery Assessment, Analysis of Real Samples and greeness evaluation
Recovery experiments at 20% spiking level showed recoveries of 66 ± 5% for marker 446 (safflower) and 53 ± 4% for marker 339 (turmeric).
The final percentage of adulteration calculated in the five samples analysed were found to be respectively 3% and 7% for turmeric and 5% and 14% for safflower, while the authentic saffron was found free of any trace of turmeric or safflower.

## Slide 12
Conclusions Case Study 1
The method is rapid, high-throughput, and environmentally friendly, requiring no chromatographic separation and allowing analysis in just 30 seconds per sample.
The DART-TQ MS/MS multi-target method successfully detected saffron adulteration down to 3% for turmeric and 5% for safflower.
The inclusion of an internal standard significantly contributed to decease variability of the MS measurements improving the correlation coefficient of the calibration curve.
Efforts will be directed to extend the method to other potential adulterants to deploy a single multi-target method for the detection of several substances adulterating saffron
FUTURE PERSPECTIVES:

## Slide 13
Case Study 2
To identify and validate selected ion transitions to target histamine in tuna.
Food safety:
determination of biogenic amines in tuna fish, with a focus on histamine.
2
Gain insights into our novel multi-target analytical approach for biogenic amine profiling in tuna — see our poster for full details.

## Slide 14
Food safety:
determination of biogenic amines in tuna fish, with a focus on histamine.
2
As well known, histamine is a key safety marker in tuna and other scombroid fish and high levels of histamine could account for an intoxication in sensitive consumers also known as scombroid poisoning.
To protect consumer health, EU Regulation (EC) No. 2073/2005 sets a maximum histamine level of 200 mg/kg in fishery products.
Biogenic Amines: A Hidden Threat to Food Safety and Human Health

## Slide 15
Food safety:
determination of biogenic amines in tuna fish, with a focus on histamine.
2
Histamine extraction optimization
01
02
1 g in 5 mL of MeOH 0.1 M HCl. Homogenization for 60 seconds.
Extract refrigeration for 30 minutes;
Centrifugation and supernatant collection and evaporation.
Reconstitute in 200 µL of MeOH/H₂O (80:20, v/v), 0.1 M HCl.
03
04
05
DART-MS parameters optimization
Full-scan and Product Ion Scan experiments
Parameters optimization
MRM experiments
Histamine calibration was performed with standard concentrations ranging from 200 to 1000 mg/kg.
06
Materials and Methods
Full-scan and product ion scan experiments facilitated the identification of potential marker compounds, initially in standard reference powders and subsequently confirmed in tuna matrix.

## Slide 16
Preliminary study on histamine standard powder and selection of potential marker
Food safety:
determination of biogenic amines in tuna fish, with a focus on histamine.
2
Results
Precursor m/z | Product m/z | Optimized CE (eV)
111,9 | 95,0 | 20
Product Ion Scan Spectrum
LOD (mg/L) | LOQ (mg/L)
83 | 278

## Slide 17
Food safety:
determination of biogenic amines in tuna fish, with a focus on histamine.
2
Results
Linearity
Recovery
LOD (mg/kg) | LOQ (mg/kg)
206 | 688
 | CV%
Interday | 23,40
Intraday | 32,55
Precision
5 replicates in the same day and in 3 consecutive days

## Slide 18
Conclusions Case Study 2
A calibration curve from 200 to 1000 mg/kg confirmed the method’s accuracy and reliability for histamine quantification.
However, further validation across diverse food matrices (e.g., fish, fermented products) is necessary to confirm its applicability.
DART-TQ-MS is a promising tool for rapid food screening, with potential for broader applications to contaminants and residues.

## Slide 19
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Strengths and Limitations of the Analytical Method
 | Advantages | Disadvantages / Limitations
Sensitivity | ✅ High sensitivity for both adulterants and contaminants | ❌ Potential matrix effects in complex samples
Speed | ✅ Real-time analysis (no chromatography required) | ❌ Limited separation of isomeric compounds
Sample prep | ✅ Minimal to no sample preparation required | ❌ Not always suitable for very fatty or highly complex matrices
Versatility | ✅ Applicable to both adulteration markers and chemical contaminants | ❌ Requires individual optimization for each new analyte or matrix
Specificity | ✅ MRM allows high selectivity for targeted compounds | ❌ Restricted to compounds with known diagnostic transitions
Scalability | ✅ Potential for high-throughput screening | ❌ Extensive validation needed for regulatory implementation

## Slide 20
Thank you for
your attention